## Slide 1: IPC 1751 Standard for Common Business Information Exchange
A brief summary
1751
A brief summary
Notes: <number>

## Slide 2: Historically used for Material Data Exchange
Electronic Equipment Manufacturers want to
  Ensure products do not contain banned / restricted materials.
  May want to know about the presence of other materials for other reasons:
    Recyclability and circularity
    Sustainability targets/goals
    Green marketing
    WEEE
    Manufacturing floor parts control and other connected factory processes
With data, product decisions can be made
  Information based on manufacturing and process knowledge
  Provides an alternative to costly testing regimes
Notes: <number>
Material declarations have become one of the major methods which companies prove their compliancy to regulatory requirements surrounding restricted chemicals and materials or what I generally call product stewardship. It can be a baseline for companies up and down the supply chain to determine their product compliancy as well as show due diligence on their part to product stewardship requirements.

## Slide 3: Why the IPC 1751 Standard
Many different data management solutions are used across the supply chain
These data management solutions must work together
Establish standard electronic data formats
Support the exchange of Materials Declaration information between trading partners (B2B)
Reduce burden on the supply chain
Notes: <number>
This standard is to help manage the various methods data is currently exchanged in the electronics industry.
Example – current burden on the supply chain looks like: (next slide)

## Slide 4
Notes: It is a paperwork monster… a nightmare without standardization

## Slide 5: The IPC 1751 Standard
<number>
The IPC 1751 standard is a data exchange top level business information and common data exchange set of definitions for suplly chain data exchange and use internally of such data also
  Designed to help the electronics industry comply with the regulations effecting their products
  Companies can understand if possible materials of concern are contained in their products
  Allows companies to make more accurate assessments of their products in an environmentally conscious society

## Slide 6
IPC 175x
JSON FORMAT
IPC 175x Advantages
Over Current Data Request Formats
Customer
(Requestor)
Supplier
(Sender)
100's - 1000's of Different Types
Current methods for data requests
  There are almost as many different types of forms as there are customers requesting data
Using the IPC 175x format allows 2 ways to exchange data
  Request/Reply-customer sends request and supplier sends reply to request- customer part numbers and manufacturer part numbers are includable
  Distribute mode
    Supplier creates a declaration that can used by anyone (no customer part numbers)
Time Consuming Efforts
Data can reside
In ANY format
Data can reside
In ANY format
Notes: <number>
The most important aspect of the 175x standard is it allows data in any format within the supply chain to be exhanged in a common format.
No ‘interpretation’ of each company form required
Allows automation of the data exchange – little to no human involvement which reduces errors
Customer request and data can be mapped to the 175x standard and the request made to the supplier
Supplier can receive the request, map its data and upload its product information into the 175x xml data format
Requestor can upload the 175x xml data into its internal data tools for acceptance/processing

## Slide 7: Example of a sectional:The IPC 1752 Standard
<number>
Company information (required)
IPC 1752 was designed to help industry comply with the restricted substance regulations effecting the electronics industry
  Data exchange companies can use it to transfer information on materials contained in their product from an upstream supplier to a downstream requestor
    Yes/No compliancy to a stated regulatory requirement
    “Negative” declaration for a list of substances not contained within the product
      If contained, amount in mass and/or ppm may be required over maximum concentration values
    Full declaration of materials actually contained in the product
  EU RoHS compliance and exemptions
  EU REACH
  China RoHS
  Korea REACH
  Other worldwide regulations
Manufacturing information
Notes: What the 1752 allows are
A very simple yes/no compliancy to a regulatory requirement,
a negative declaration stating these products do not contain the JIG-101 list of substances above regulatory thresholds. This is still a yes/no query, but with more details on the types of materials. Where contained above the threshold further information can be supplied. is required.
Full declaration capabilities up to the homogeneous level

## Slide 8: 175x
Full system approach
  Integrates all types of supplier declarations into one framework with modularized information:
    Business Information – 1751
    Material - 1752
    Manufacturing – 1756
    Laboratory Report -1753
    Conflict minerals – 1755
    Process chemicals (coming) -1757
  Uses Extensible Markup Language (XML) in past
  Currently migrating to JSON (Javascript Object Notation)
Notes: Where the previous version of the 1752 material declaration contained all the business, legal, product, material and manufacturing information in a single declaration model, the 175x series has split them out into separate modules.
The 1751 contains the business information (requestor and supplier), the legal statement and signatures and what other types of modules will accompany this information.
The 1752 is the material declaration that includes compliance queries such as EU RoHS, China RoHS and REACh.
The 1756 is the basic manufacturing information needed by PCB assembly companies.
UML = Unified Modeling Language

## Slide 9: 1751 and example sectionals
JSON schema supported by industry stakehokders including 3rd party suppliers
1751: Controlling Requirements
    Supplier / Requestor info
    Legal statements
    Component name(s) & weight(s)
      Support multiple parts
    Modules available (1752 – A, B, C and/or D, 1753, 1755, coming 1757, etc.)
  1752: Material Declaration
    Class A = Yes/No Type of declaration (EU, China, REACh and/or others)
    Class B = Material Group Level ONLY (Not used)
    Class C = Product Level – Yes/ No to substance categories/substances above threshold
    Class D = Subproducts, Material Level and Substances)
  1757: Process chemicals

## Slide 10: 1751 a few new notable adoptions
Support for multiple parts
  Part families and part ranges
  Multiple levels
A generalized declaration query list supports
  requester queries
  Future regulations
Improved Modularity
  Different sectionals going forward to include conflict minerals, process chemicals, recycling, circularity, energy usage, greenhouse footprints, connected factory in-house processes etc.
Supports verifiable credentials using DID or S2S (system to system based on JWT) and other VC
  Different sectionals going forward to include conflict minerals, process chemicals, recycling, circularity, energy usage, greenhouse footprints, connected factory in-house processes etc.
Document classification
  Internal or external or both are some options, and these can be further added on.
All definitions extendable or more restrictable
  Different sectionals can extend the 1751 definitions, adopt as is or further restrict value permissible.
Notes: Updates to the 175x series is allowance for multiple part declarations, ability to have more generalized query lists, not just EU RoHS. With the separate modules it can be clearly understood what information is being provided. With these updates the electronic signature resides within the XML data, not in the original PDF form only.

## Slide 11: Example:1752 v2 Classes
Class | Description | Declaration Type | Detailed Requirements
A | -Reporting in Query/Reply format | Query/Reply | - Supplier states whether the product meets defined query list
B | Material group reporting (not used) | Material Group | - Supplier states the amount of different groupings of materials within a product.
C | - Substance categories and/or substances reporting at the product level | substance categories | - Supplier provides mass and/or concentration of substance category and/or substances at the product level if above thresholds.
D | - Materials and Substances reporting at the homogeneous material level | Full substances | - Supplier provides location, mass, and/or PPM of substances at homogeneous material level - Can include subproducts/parts
Notes: Within the 1752 module, there are 4 classes of information that can be provided
Class A: Query List
Class B: Higher level material summarization (this one is new)
Class C: Yes/No material declaration based on the JIG-101 material list plus REACH substance list
Class D: Full material declaration capabilities at the homogeneous level

## Slide 12: Example of modularity:1752 – Class A Query List Declaration and 1755 Conflict minerals
Uses multiple “query” statements with (example) Boolean true/false response for some 1752 queries and string for conflict minerals
Eases the addition of declarations to support new legislation
  Can be added without modifying the JSON
  Easy for the solution providers to adapt to new declarations
  Allows requester to provide custom declaration queries
Notes: There are more than just EU RoHS compliancy questions being asked since the original release of the 1752 standard. This query list allows for additional true/false query questions to be asked such as EU RoHS, China RoHS and REACh compliancy.

## Slide 13: Data Entry Tool
Separation of data and tool
  Schema available for companies and 3rd party solution provider to develop and support tools
  Solution provider verification peer review process
  Schema and JSON standard will ensure easy data transfer from one tool to another
Notes: As stated earlier, a significant change from 1752 v1x to the 175x v2 series is the separation of the data entry tool. Where 1752 v1x was based on the Adobe Acrobat visual tool, the 175x v2 series will rely on 3rd party solutions. This allows the focus of the standard to be on the schema and data it contains, not on developing a software tool (and all its bug fixes & updates).
The United States National Institute of Standards and Technology is providing a tool called Scriba for 3rd party suppliers or individual companies for humans to see the data and test the schema. This tool is open source and can be used to develop in-house tools or even become part of a 3rd party solution provider’s software release.

## Slide 14: S2S (system to System) proposed support
Satisfying requirements for verifiable credentials (VC)
  Uses JWT (JSON web tokens)
  Use of Bearer token-Enables open and easy process for Solution provider verification peer review. Follows commonly used protocol in manner easy for peer review verification.
  Draft JSON Schema created
  1751 supports this across entire ecosystem by having an attribute to docID (which exited before) to add docClas which stands for classifying a document, so to allow control for operations and security.
Notes: As stated earlier, a significant change from 1752 v1x to the 175x v2 series is the separation of the data entry tool. Where 1752 v1x was based on the Adobe Acrobat visual tool, the 175x v2 series will rely on 3rd party solutions. This allows the focus of the standard to be on the schema and data it contains, not on developing a software tool (and all its bug fixes & updates).
The United States National Institute of Standards and Technology is providing a tool called Scriba for 3rd party suppliers or individual companies for humans to see the data and test the schema. This tool is open source and can be used to develop in-house tools or even become part of a 3rd party solution provider’s software release.

## Slide 15: Conclusion
IPC1751 provides flexible approach including
  Every type of part information need by industry-Multiple parts in a single documents with multiple includes of sectionals for each appropriate case.
  Tool independent data exchange
  .

## Slide 16: Other Information
More information and actual schemas
  https://www.ipc.org/materials-declaration-data-exchange-standards-homepage
Presenter- My contact information:
Dr. N. Nagaraj, Chief
Papros Inc.
shaka777@gmail.com
Notes: As stated earlier, a significant change from 1752 v1x to the 175x v2 series is the separation of the data entry tool. Where 1752 v1x was based on the Adobe Acrobat visual tool, the 175x v2 series will rely on 3rd party solutions. This allows the focus of the standard to be on the schema and data it contains, not on developing a software tool (and all its bug fixes & updates).
The United States National Institute of Standards and Technology is providing a tool called Scriba for 3rd party suppliers or individual companies for humans to see the data and test the schema. This tool is open source and can be used to develop in-house tools or even become part of a 3rd party solution provider’s software release.

## Slide 17
Questions?